## Slide 1: Rocky River Drive Plan
Northeast Ohio Areawide Coordinating Agency
Kamm’s Corners Development Corporation

## Slide 2: Rocky River Drive Plan Goals
Identify transportation improvements for motorists, pedestrians, transit riders, and cyclists
Improve gateways to the neighborhood and connections to Cleveland Hopkins, Rocky River Reservation
Update 2002 Master Plan to reflect trends in property values, foreclosures, vacancy in order to develop a redevelopment strategy
Analyze options for City owned parking at Albers and West 168th Street

## Slide 3: Timeline
2014 Deliverables | Completion
Outline project goals and objectives, | May 2014
Identify Steering Committee members | June 2014
Steering Committee Meeting #1 | June 2014
Existing Conditions Summary | September 2014
Community Meeting #1 | September 2014
Draft list of recommendations | November 2014
2015 Deliverables | Completion
Steering Committee Meeting #2 | January 2015
Draft prioritized implementation plan | March 2015
Community Meeting #2 | March 2015
Finalize list of recommendations | April 2015
Develop draft report | May 2015
Steering Committee Meeting #3 | May 2015
Finalize prioritized implementation plan | June 2015
Final report | June 2015
City Council and Planning Commission adoption | June 2015

## Slide 4: Study Area
2002 Master Plan
Current Study

## Slide 5: Community Amenities and Destinations
Identified in 2002 Master Plan
Since 2002, neighborhood assets have strengthened
  Cleveland Clinic
  Kamm’s Corners
  St. Patrick’s Church
  Rocky River Reservation

## Slide 6: Population and Housing Trends
Chart: Age Characteristics 1980 - 2010
| Under Age 18 | 18 to 24 | 25 to 44 | 45 to 64 | 65+
1980 | 5534 | 2364 | 5085 | 4030 | 2439
1990 | 4219 | 1305 | 5583 | 3320 | 2615
2000 | 3546 | 972 | 4960 | 3074 | 2318
2010 | 3200 | 1236 | 4022 | 3932 | 1668
Overall, population is declining
  Slowing between 2000 – 2010
  Growth in young adults and adults
Population, Household, and Dwelling Units 1980 - 2010 |  |  | 
 | Population | Households | Dwelling Units
2010 | 14,058 | 6,088 | 6,567
2000 | 14,870 | 6,347 | 6,558
1990 | 17,042 | 6,802 | 7,118
1980 | 19,452 | 6,758 | 6,913
Change 1980-2010 | -28% | -10% | -5%
Age Characteristics 1980 - 2010 |  |  |  |  |  | 
 | Under Age 18 | 18 to 24 | 25 to 44 | 45 to 64 | 65+ | Total
1980 | 5,534 | 2,364 | 5,085 | 4,030 | 2,439 | 19,452
Percent of Total | 28% | 12% | 26% | 21% | 13% | 100%
1990 | 4,219 | 1,305 | 5,583 | 3,320 | 2,615 | 17,042
Percent of Total | 25% | 8% | 33% | 19% | 15% | 100%
2000 | 3,546 | 972 | 4,960 | 3,074 | 2,318 | 14,870
Percent of Total | 24% | 7% | 33% | 21% | 16% | 100%
2010 | 3,200 | 1,236 | 4,022 | 3,932 | 1,668 | 14,058
Percent of Total | 23% | 9% | 29% | 28% | 12% | 100%

## Slide 7: Property Characteristics
Land use has not significantly changed
  Majority single family housing and apartments
  Retail and commercial services located in nodes in some areas
    Mixed with housing in others
2002 Master Plan

## Slide 8: Property Values
Median Year Structure Built | 
Census Tract | Average
1236.01 | 1937
1236.02 | 1951
1236.03 | 1928
1237 | 1950
1238 | 1941
4355 Properties total in study area (quarter mile radius)
Minimum: $0
Maximum: $87,719,100
Average: $79,720

## Slide 9: Building Conditions on Rocky River Drive

## Slide 10: On and Off Street Parking

## Slide 11: Albers Public Parking Lot
City owned lot behind Kamm’s Corners (southeast corner of Lorain and Rocky River Drive)
~145 spaces
  In Kamm’s Corners parking is in high demand
In need of resurfacing and lighting
Needs maintenance and improvement plan
Site of special events, e.g. Kamm’s Corners Farmer’s Market

## Slide 12: Street Sections and Lane Widths
Typical road width is 52 feet
  Outer lanes widen south of Puritas
Average Daily Traffic around 16,000 vehicles
  Higher volume closer to Lorain

## Slide 13: Crashes: Lorain to Puritas & Puritas to Brookpark

## Slide 14: Sidewalks and Crosswalks
Sidewalk coverage is almost complete
  Small sections missing on Cleveland Parkway
Condition is generally fair
  Some utility poles and fire hydrants obstruct traffic
  In areas curb is crumbling
Sediment, gravel, debris can pose hazard to pedestrians and cyclists
Curb ramps are not all ADA compliant
Crosswalk signals do not indicate “walk” without pushing button in places
  In some places button does not work

## Slide 15: Bicycle Infrastructure
Existing:
  Metroparks Multiuse Path
  Puritas Avenue Bike Lanes
Plans:
  Puritas connector to Metroparks
  Lorain Avenue east of W. 150th
  Triskett Road (W. 140th to Lorain)
Proposed (by Cleveland Bikeway Implementation Plan)
  Rocky River Drive
  Connectors to Grayton Road and Cleveland Hopkins Airport

## Slide 16: Public Transportation
Number 86 bus connects West Park and Brookpark Rapid Transit Stations, south to Berea
Weekdays: Departs once an hour (north and southbound) between 4:51 am and 10:37 pm
Weekends: Departs once an hour (north and southbound) between 5:38 am and 7:35 pm
Number 22 bus provides service to Cleveland Hopkins airport between 12:56 am and 3:56 am, when the Rapid is not running
  Once an hour departure
Most stops are not sheltered in study area

## Slide 17: Public Transportation
Ridership (# One Way Trips) | Route 78 | Route 86
2013 Annual Ridership | 412,512 | 151,685
Average Weekday Ridership | 1,612 | 572
Destination Type (% Trips on Average Weekday) | # 78 | # 86
Home | 44% | 51%
Work | 25% | 24%
Social Visit | 11% | 8%
School (K-12) | 6% | 1%
College-University | 3% | 5%
Doctor's Appointment | 3% | 0%
Shopping | 3% | 5%
Errand (bank, post office, etc.) | 2% | 0%
Recreation/Sightseeing | 1% | 5%
Restaurant | 1% | 0%
Other | 2% | 1%
Driver’s License | # 78 | # 86
Yes | 38% | 29%
No | 62% | 71%
Access Mode | # 78 | # 86
Walked | 63.6% | 47.2%
Biked | 0% | 0.3%
Dropped Off | 0.6% | 0%
Wheelchair/Scooter | 0.2% | 1.0%
Transferred from Red Line (W.117th) | 11.1% | -
Transferred from Red Line (Puritas) | 12.5% | -
Transferred from Red Line (West Park) | - | 19.1%
Transferred from Red Line (Brookpark) | 1.1% | 18.5%
Public Transit Usage (Days/Week) | # 78 | # 86
0 | 1% | 1%
1 | 3% | 5%
2 | 4% | 3%
3 | 9% | 5%
4 | 14% | 11%
5 | 37% | 52%
6 | 11% | 17%
7 | 22% | 8%

## Slide 18: Community Feedback
One Word Impression:

## Slide 19: Community Feedback
Chart: Participants Consider the Rocky River Drive Corridor:
| Comfortable | Connected | Convenient | Important | Isolated | Safe | Unpleasant | Unsafe
Total | 16 | 47 | 84 | 102 | 31 | 25 | 58 | 37

## Slide 20: Community Feedback
Best Locations
Worst Locations

## Slide 21: Community Feedback
Chart: Participants Ride the Bus on Rocky River:
| Never | Occasionally
Total | 140 | 11
Chart: Participants Would Use Transit More If it Were More:
| Attractive | Cheaper | Clean | Convenient | Faster | Intuitive | More Frequent | Safe | Other
Total | 28 | 18 | 33 | 52 | 28 | 13 | 34 | 50 | 30

## Slide 22: Community Feedback
Chart: Participants Walk Along Rocky River Drive:
| Never | Occasionally | Regularly
Total | 32 | 87 | 35
Chart: Participants Feel Traffic Is a Problem:
| Never | Occasionally | Regularly
Total | 28 | 96 | 27

## Slide 23: Community Feedback
Chart: Participants Would Like to See New:
| Apartments | Entertainment | Green Space | Restaurants | Senior Living | Shopping | Social Services | Townhomes | Other
Total | 19 | 70 | 105 | 120 | 33 | 100 | 9 | 69 | 30
Chart: Participants Would Like to See Improved:
| Benches | Bicycle Amenities | Cleaner Sidewalks | Gateway to/from Airport | Lighting | Metroparks Connections | Neighborhood Signage | Property Maintenance | Public Art | Snow Plowing | Streetscape Repairs/Improvements | Transit Stop Enhancements | Trees and Landscaping | Other
Total | 52 | 43 | 87 | 68 | 87 | 84 | 62 | 115 | 54 | 43 | 110 | 44 | 114 | 33

## Slide 24: Preliminary Recommendations
Continue targeting commercial vacancies and abandoned homes for redevelopment or demolition
  Identify strategies to attract new businesses and reduce vacancies
  Encourage reinvestment to maintain and improve building stock
  Encourage sideyard expansions where possible
Property upkeep and renewal
  Address vacant properties for larger redevelopment projects
  Explore opportunities for new senior housing
Promote efforts to upgrade the general appearance of the corridor
  Consolidate utility poles
  Limit signage to appropriate scale and design
    Prohibit digital reader board signs
  Discuss long term strategy of CMHA properties with authority

## Slide 25: Preliminary Recommendations
Introduce more neighborhood greenspace
  Determine development potential of vacated streets (Forestdale and Midvale) with Chelm properties
  Based on negotiations, plan for passive and active recreation spaces, particularly adjacent to the Rocky River Drive Corridor
      Short term: native plantings, low maintenance
      Longer term strategy – identify recreational opportunites
    Conceptualize a rugby facility, possibly near existing baseball fields

## Slide 26: Preliminary Recommendations
Focus on mixed use nodes along Rocky River Drive
  Stategically employ Urban Overlay zoning to promote mixed use/walkability
    Cluster of commercial uses around Valleyview Drive (between Lorain and Puritas)
    Intersection of Puritas and Rocky River Drive
    Parkmount/Homeway and Rocky River Drive

## Slide 27: Preliminary Recommendations
Create neighborhood gateway on southern end of study area (consistent with wayfinding)
  New Gas Station at Brookpark and Rocky River Drive
    Will include gateway landscaping – signage to West Park, Kamm’s Corners
  Cleveland Parkway
    Denotes separation from airport uses (i.e., rental car facilities)
    Extend wayfinding to Brookpark

## Slide 28: Preliminary Recommendations
Albers Parking Lot
  Resurface parking lot, asphalt is in bad condition
  Restripe boundaries to delineate between lot area and adjacent travel lanes and private lots
  Study feasibility of installing pay station for typical daily use, can be suspended for special events (i.e., Hooley). Downtown Lakewood, Cleveland Heights are good examples
  Improve lighting for safety
  Improve signage (consistent with wayfinding and neighborhood gateway)
  Discuss management of lot by Kamm’s Corners with City of Cleveland
  Long term:
    Work with near-by property owners to identify separate lots to more efficiently use/share parking space
    Identify measures to address grade change between Albers and Walgreens lots
    Incorporate stormwater controls/green infrastructure to alleviate stormwater flooding and improve attractiveness/emulate landscaping on Lorain

## Slide 29: Preliminary Recommendations
        Albers Ave.
          Convert Albers Ave. to one-way operation (traffic flows east, enter on Rocky River, exit on West 168th)
          Allow on-street parking on both sides of street

## Slide 30: Preliminary Recommendations
  Parking
    Encourage new parking lots to be situated at the rear or side of structures by decreasing building setbacks along Rocky River Drive
    Work with property owners to better utilize under capacity parking lots, either through landscaping or redevelopment
    Study reuse options for parking lot south of Maplewood

## Slide 31: Proposed Traffic Operations: North of Puritas

## Slide 32: Proposed Traffic Operations: South of Puritas
(South of Homeway)

## Slide 33: Benefits of 3-lane Roadway
SAFETY: 29% Reduction in crashes, improved visibility for left-turning cars & crossing pedestrians, reduced speeding
LIVABILITY: driving lanes are further away from sidewalk, median could be landscaped where turn lanes aren’t needed
OPERATIONS: separating left turns reduces delay, side street through movements are easier

## Slide 34: Current Configuration

## Slide 35: Proposed Configuration

## Slide 36: Current Configuration

## Slide 37: Proposed Configuration

## Slide 38: Preliminary Recommendations
Sidewalks
  Construct sidewalk from intersection of Brookpark Road and Rocky River Drive to Brookpark Rapid Transit Station (both entrances)
  Address debris on sidewalk (trash, gravel, etc.)
  Request City of Cleveland to regularly schedule street sweeping of Rocky River Drive
  Spot repair cracked/deteriorated sidewalks through partnership with property owners and city sidewalk repair program
  Light 480 underpass and repair chain link fence

## Slide 39: Preliminary Recommendations
Bicycle Infrastructure
  Install bike lanes on Rocky River Drive (see street reconfiguration)
  Continue bike lanes on Puritas though Rocky River Drive intersection west to Rocky River Drive Reservation entrance
    Long term – explore multiuse path to connect to Metroparks facility
  Work with business owners to install bike parking
    Potential bike box on West 168th/alleyway
  Explore multiuse path from Brookpark Road/Rocky River Drive intersection to Cleveland Hopkins International Airport with City of Cleveland Department of Port Control
    Identify examples of airports with multiuse paths

## Slide 40: Preliminary Recommendations
Transit
  Replace bus stop signs with new RTA bus stop signage, which includes route information
  Consolidate bus stops where feasible
    Consolidated stops could warrant new shelters
  Ensure all bus stops have paved boarding areas
  Discuss feasibility of #86 service stopping at Cleveland Hopkins International Airport

## Slide 41: Preliminary Recommendations
Wayfinding
  Develop wayfinding that helps to identify West Park neighborhood
    Locate directionality to rapid transit stations, neighborhood centers, parks, parking
Streetscape
  Identify where street trees can be planted/replaced
  Enhance lighting on the corridor, particularly near Cleveland Parkway

## Slide 42: Next Steps
Incorporate public comments
Finalize recommendations
Develop implementation plan and preliminary cost estimates
Stakeholder Meeting 3
Draft final report

## Slide 43: Questions or Comments?
Ryan Noles rnoles@mpo.noaca.org or 216-241-2414 ext. 273
Ben Campbell ben.campbell@kammscorners.com or
216-252-6559 ext. 1200